## Slide 1
North Dallas Chamber Commerce (NDCC) Energy Forum
Pablo Vegas
ERCOT President & CEO
January 26, 2024

## Slide 2
The ERCOT Region
The interconnected electrical system serving most of Texas, with limited external connections
90% of Texas electric load; 75% of Texas land
85,508 MW peak, Aug. 10, 2023
More than 52,700 miles of transmission lines
1,100+ generation units (including PUNs)
ERCOT connections to other grids are limited to ~1,220 MW of direct current (DC) ties, which allow control overflow of electricity

## Slide 3: Texas’ Estimated Population Growth
Texas Population 2023
30,500,280*
Estimated Growth
2024: 31 million
2025: 31.4 million
2026: 31.9 million
2027: 32.4 million
2028: 32.9 million
*The last US census was in 2020, so current figures are projected based on the estimates only.
Notes: Sources: TEXAS: 2020 Census
Texas Population 2023 (Demographics, Maps, Graphs) (worldpopulationreview.com)
Texas Demographic Center
US Census State Population Estimates
US Census County Population Estimates
American Community Survey (2009 - 2013)
Census QuickFacts

## Slide 4: 2022-2023 Summer Peak Demand Records
Key Takeaway: Peak demand for summer increased drastically over the last two years. Summer 2023 had 49 days with a peak higher than 80 GW (the previous all-time peak demand).
Days Over 80 GW Peak |  |  | 
Month | 2021 | 2022 | 2023
June | 0 | 0 | 4
July | 0 | 1 | 15
August | 0 | 0 | 26
September* | 0 | 0 | 4
2022
2023
85,508

## Slide 5: The ERCOT Electric Grid: Capacity and Demand
85,508 MW
(August 10, 2023)
2000 Generating Capacity
2024 Generating Capacity
2000
All-Time Peak Demand Record
57,606 MW
As of January 2024
All-Time Peak Demand Record
48% increase
Chart: 







Chart: 
| 2022
Natural Gas | 0.666
Wind | 0.002
Coal | 0.246
Solar | 0
Nuclear | 0.071
Storage | 0
Other* | 0.0006
Hydro | 0.0045557
*Includes biomass-fired units and DC Tie capacity
*Includes biomass-fired units and DC Tie capacity
Chart: 
Fuel Types | 0
Natural Gas | 0.443
Wind | 0.252
Coal | 0.098
Solar | 0.132
Nuclear | 0.035
Storage | 0.027
Other* | 0.01
Hydro | 0.004
Notes: 2000 data: reflects the forecasted operational installed capacity, based end of year 2000 data from ERCOT Installed Capacity Mix Trends
2024 data: reflects operational installed capacity based on December CDR report for Summer 2024.
Peak demand: 48% increase from the 2000 peak demand of 57,606 MW to 85,508 on August 10, 2023

## Slide 6
The ERCOT Electric Grid: Then and Now
Notes: Where we have been

## Slide 7: Weatherization
Total as of December 2023
1774 weatherization inspections
(1264 generation resources and 510 Transmission Service Providers (TSP) facilities)
ERCOT conducts weatherization inspections of generating and transmission facilities. Weatherization inspections are tracking well ahead of the required rate of 1800 inspections over 3 years to meet 2024 goal.
Chart: 
| 31-Dec-21 | 31-Mar-22 | 30-Jun-22 | 30-Sep-22 | 31-Dec-22 | 31-Mar-23 | 30-Jun-23 | 30-Sep-23 | 31-Dec-23 | 31-Mar-24 | 30-Jun-24 | 30-Sep-24 | 31-Dec-24 | GOAL
Cumulative Inspections (Current) | 324 | 324 | 324 | 324 | 583 | 1098 | 1200 | 1648 | 1774
Goal | 138.4615 | 276.9231 | 415.3846 | 553.8462 | 692.3077 | 830.7692 | 969.2308 | 1107.6923 | 1246.1538 | 1384.6154 | 1523.0769 | 1661.5385 | 1800 | 1800

## Slide 8: Transmission Planning Summary
As of October 12, 2023, projects energized in 2023 total about $1.533 billion.
  $1.567 billion energized in all of 2022
As of December 31, 2023, ERCOT has endorsed transmission projects totaling $3.231 billion.
  Total endorsed transmission projects in 2022 equaled $3.311 billion
As of October 12, 2023, projects in engineering, routing, licensing, and construction total about $13.537 billion
Chart: RPG Projects Endorsed ($ million) in Each Year
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
$ Million | 653 | 890 | 611.85 | 628.8 | 1043.29 | 2498.85 | 3311 | 3231
#REF! | 1
Notes: Data from RMC December 18, 2023, presentation

## Slide 9: Illustration of Long-Term Resource Adequacy Issue (Summer)
(Note: Resource Value is the installed capacity of a resource type multiplied by its Effective Load Carrying Capability (ELCC), ELCC is the amount of the resource type relative to theoretical 100% available capacity, that can serve load without reducing system reliability; that is, not increase the expected occurrence of unserved load. ELCC will always be less than 100 percent. (2300 MW of dispatchable generation is held for emergency reserves).
Dispatchable Thermal Generation
ELCC
@ Peak Load
Wind ELCC
@ Peak Load
Solar ELCC
@ Peak Load
Battery Storage
@ Peak Load
Summer
Load (MW)
Dispatchable Thermal Generation
(2000-2008) more than 20,000 MW of net new dispatchable thermal generation added to the grid.
(2008-2022) only 1,500 MW of net new dispatchable thermal generation added.
20,925 MW retired
22,485 MW added
More than 48,000 MW of net new solar and wind added (2008-2022).
Total Thermal Fleet is 77,040 MW
41% is older than 30 years (31,863 MW) (1993)
27% is older than 40 years (21,148 MW) (1983)
12% is older than 50 years (9,586 MW) (1973)
2% is older than 60 years (1,737 MW) (1963)
MW Resource Value vs Summer Peak Load for Operational and Planned Generation Capacity
9

## Slide 10: Generation Interconnection Requests
A break-out by zone can be found in the monthly Generator Interconnection Status (GIS) reports available on the Resource Adequacy Page: http://www.ercot.com/gridinfo/resource
*Other includes petroleum coke (pet coke), hydroelectric, fuel oil, geothermal energy, other miscellaneous fuels reported by developers, and fuel cells that use
fuels other than natural gas.
Chart: 
| Gas | Wind | Solar | Battery | Other*
2023 | 3.0121 | 7.9172 | 11.0297 | 5.0297 | 0
2024 | 2.8253 | 4.9563 | 34.2252 | 36.8037 | 0.01803
2025 | 3.3859 | 5.9234 | 51.4568 | 41.297 | 0.203
2026 | 1.603 | 3.4376 | 26.7713 | 24.1736 | 0.635
2027 | 0 | 1.417 | 6.2423 | 1.7931 | 0
2028 | 1.35 | 0 | 1.1321 | 0.28244 | 0.2
2029 | 0.3 | 0 | 0 | 0 | 0
2030 | 0 | 3.5 | 0 | 0 | 1.232
1,671 active generation interconnection requests totaling 325,215 MW as of December 23, 2023.
                Solar: 145,654 MW
                Wind: 34,591 MW
Gas: 15,483 MW
Battery: 127,068 MW
Notes: As of December 23, 2023

## Slide 11: Nuclear Dispatchable Generation
August 16, 2023: Gov. Abbott letter directed the PUCT to establish working group to study and plan for nuclear reactors in Texas, to:
    Understand states’ role in deploying advanced nuclear reactors for grid reliability
    Determine nuclear-specific changes in ERCOT market; regulatory impediments to development; permitting for building reactors.
    Coordinate with stakeholders on timely implementation of reactors.
    Identify any federal incentives for Texas and stakeholders.
    Working group will coordinate with ERCOT to solve technical challenges of incorporating nuclear energy into the ERCOT grid.
September 28, 2023: Texas Advanced Nuclear Reactor Working Group: Commissioner Jimmy Glotfelty convened first public working group
  Proposed organizational structure and work plan necessary to carry out Gov. Abbott’s directive to plan for the use of advanced nuclear reactors in Texas.
  December 1, 2024: Working Group to submit plan and recommendations to Gov. Abbott on how Texas will be come the national leader in using advanced nuclear technology.
Notes: Reference: https://gov.texas.gov/uploads/files/press/Jackson,_Kathleen_08.16.23.pdf
TX Advanced Nuclear Reactor Working Group Sept 28 workshop.pdf